## Slide 1: MicroPython with LoPy
Getting started workshop @ MakeZurich

## Slide 2: What is MicroPython
Python for Microcontrollers
Lean implementation of Python 3
Subset of standard lib
Needs
  256k code space
  16k RAM

## Slide 3: What is a LoPy
ESP32 Board
  160 MHz CPU
  512k RAM
  4 MB Flash for user code
  I2C, SPI, UART, I2C
  SD Card
  8 ADC Channels
  24 GPIOs
  RTC
  WS2812 LED
Wireless connectivity
    Bluetooth 4.2 (BLE & Classic)
    LoRa (Semtech’s SX1272)
    WiFi

## Slide 4: Tooling
Batteries included!
  Firmware upgrade tool
  PyMakr IDE
  PyMate mobile App
    Based on MQTT
  Soon: cloud service
Code upload via
  Built-in FTP/telnet Server
  Serial connection

## Slide 5: First thing to do
Install Pycom updater
  https://www.pycom.io/support/supportdownloads
Firmware Upgrade!
  Almost weekly releases with new features
  Check http://forum.pycom.io Announcement topic

## Slide 6: Connect to Device REPL
PyMaker IDE
  Settings/Preferences/Pycom Device
Directly via serial port
  8N1 / 115200 Baud
  screen /dev/tty... 115200
  putty
WiFi
  SSID: lopy-wlan-XXXX
  Password: www.pycom.io
  Telnet 192.168.4.1

## Slide 7: Hello World!
>>> import pycom >>> pycom.heartbeat(False) >>> pycom.rgbled(0xFF0000)
>>> print(‘Hello World’)
REPL (read-evaluate-print-loop)
Interactive interpreter (>>>)
pycom.rgbled(0xRRGGBB)

## Slide 8: Primer on Python
Variables
Functions
text = ‘Dont forget your towel!’
number = 42 floatingnumber = 13.37
def print_text(name, age):
text = "My name is {0} and I’m {1} years old"
print(text)

## Slide 9: Primer on Python (math)
Addition, Subtraction, Division, Multiplication, exponentiation
12+34 3*3
16/2
(3+1)*(4+5)
5**2 #5 to the power of 2
‘spam’*3 #spamspamspam

## Slide 10: Primer on Python (useful built-ins)
print(text) – Print text
int(text) – «cast» text to int
type(obj) – Get type of object
input(prompt) – Read from stdin return value as string

## Slide 11: Primer on Python (containers)
Lists
  mylist = [1,2,3,4]
  mylist.append(5)
  mylist.remove(2)
Dictionaries
  mydict = {‘name’: ‘zaphod beeblebrox’, ‘heads’:1}
  mydict[‘heads’] = 2

## Slide 12: Primer on Python (control structs)
if value == True:
print(‘value is true’)
else:
print(‘value is false’)
while True:
do_whatever_is_to_do()
for i in range(10):
print(‘{0}-th run’.format(i))

## Slide 13: Time Module
import time
time.sleep(10) #sleep 10 seconds time.sleep_ms(200) #sleep 20 milliseconds

## Slide 14: Exercises
Create a function which changes the LED color from red to blue every 1s
Create a function which asks for your weight and your body size and calculates BMI = weight (kg) divided by size2 (m)

## Slide 15: Primer on Python (modules)
Files are treated as modules
Stuff is imported from modules
Stuff needs to be imported to be used
File lib.py contains function connect()
# use lib
from lib import connect
Print_name()
# lib.py def print_name(name):
print(‘------------’) print(name)
print(‘------------’)

## Slide 16: More on Python
Lots of tutorials
https://docs.pycom.io
https://learnpythonthehardway.org/
http://docs.python-guide.org/en/latest/intro/learning/

## Slide 17: GPIO output
from machine import Pin
# initialize ``P9`` in gpio mode and make it an output
p_out = Pin('P9', mode=Pin.OUT)
p_out.value(1)
p_out.value(0)

## Slide 18: GPIO input
from machine import Pin
# initialize ``P10`` in gpio mode and make it an input
p_in = Pin('P10', mode=Pin.IN, pull=Pin.PULL_UP)
p_in.value() # get value, 0 or 1

## Slide 19: GPIO with interrupts
from machine import Pin
# initialize ``P10`` in gpio mode and make it an input
p_in = Pin('P10', mode=Pin.IN, pull=Pin.PULL_UP)
p_in.callback(Pin.IRQ_HIGH_LEVEL, lambda pin: print(“ON”)) p_in.callback(Pin.IRQ_LOW_LEVEL, lambda pin: print(“OFF”))
# Pin.IRQ_HIGH_LEVEL | Pin.IRQ_LOW_LEVEL also possible

## Slide 20: GPIO numbering
# Numbering with expansion board
Pin.exp_board.G16
led = Pin(Pin.exp_board.G16, mode=Pin.OUT)
# Numbering without expansion board # P10 is mapped to the Button
Pin.module.P9
led = Pin(Pin.module.P9, mode=Pin.OUT)

## Slide 21: Pin Diagramms
Expansion board https://www.pycom.io/wp-content/uploads/2016/11/expansion_v02_pinout.pdf
LoPy https://www.pycom.io/wp-content/uploads/2016/11/lopy_pinout.pdf

## Slide 22: Exercise
React to button presses on P10 and turn on/off on P9
Do the same with interrupts!

## Slide 23: Boot process
/flash/booty.py
/flash/main.py

## Slide 24: Nice to know
Deploy your scripts via
  telnet
  FTP
Safe boot mode
  Firmware recovery

## Slide 25: Hello ThingsNetwork!
from network import LoRa
import socket
# Initialize LoRa in LORAWAN mode.
lora = LoRa(mode=LoRa.LORAWAN)
# join a network using ABP (Activation By Personalization)
lora.join(activation=LoRa.ABP, auth=(dev_addr, nwk_swkey, app_swkey))
# create a LoRa socket
s = socket.socket(socket.AF_LORA, socket.SOCK_RAW)
# make the socket blocking
# (waits for the data to be sent and for the 2 receive windows to expire)
s.setblocking(True)
# send some data
s.send(bytes([0x01, 0x02, 0x03]))
# make the socket non-blocking
# (because if there's no data received it will block forever...)
s.setblocking(False)
# get any data received (if any...)
data = s.recv(64)
print(data)

## Slide 26: Get DeviceEUI
import binascii
from network import LoRa
lora = LoRa(mode=LoRa.LORAWAN)
devEUI = binascii.hexlify(lora.mac())

## Slide 27: Libraries
https://github.com/micropython/micropython-lib
Useful things
  urllib
  urequests
  MQTT client

## Slide 28: What is there?
https://docs.pycom.io/pycom_esp32/library/index.html
I2C
ADC / DAC
OneWire
PWM
SPI
Watchdog (WDT)
SD Card
Timers
RTC
Bluetooth GATT
Multithreading

## Slide 29: Thanks!
  Hope we could wetten your appetite 
  If you have any questions dont hesistate to contact me
  Christian.faessler@adnexo.ch